Blastrac 6-55DC

|  | Blastrac's Deluxe Six Cartridge Auto Pulse Professional Vacuum is the preferred vacuum for the professional contractor requiring continuous operation and high performance. This is the Cadillac® of industrial dust collection. This system features: Six cartridge system is set to pulse the filters every 15 seconds Work without performance loss An available electrical outlet on the dust collector Standard side removal dust cartridges to aid in the clean disposal of used dust An optional screw conveyor dust bin and bagging system An optional HEPA filtration unit for hazardous material handling Application For use with large surface preparation jobs, including shotblasters, scarifying, and grinding. |
| --- | --- |

Technical Specs Dust Collectors Overview Accessories Part Number: 6-55DC Voltage 460V 3P Amperage 11A *Maximum Air Flow 1000 CFM *Maximum Static Pressure 21 Inches H20 *Dust Bin Capacity 250 lbs Vacuum Hose Diameter/Length 5"/6" x 60 Feet Dimensions (LxWxH) 68" x 32" x 53" Weight 1433 lbs